## Slide 1: Technical Discussions
05-15-2026

## Slide 2: SLAM-SIG Domain Selection
The PTS teams were scoped to use the UW-developed SLAM domains for the validation basins (ARC, COMPASS, and STARR II, 2025) .
  See Wright et al. (2025) for additional details on the development of the SLAM domains.
Each PTS team reviewed the SLAM‑SIG transposition domains following SOP Section 5.10.1.2.1 (FEMA & USACE, 2025) and determined that the domains did not pass the review.
  This was documented as an area for further investigation in FEMA Innovations SO3.2 Project Backlog.
  See STARR II (2026) and FEMA et al., (2026 a-d) for additional details
To maintain progress, FEMA directed the PTS teams to select a SLAM‑SIG domain for each basin using a consistent method (FEMA et al., 2026d).
The following discussion outlines the selection process and presents the SLAM‑SIM domains selected for each basin.
Notes: Erica

## Slide 3
SOP Volume II, Section 5.3
The fundamental assumption made by using SST is that a region of homogeneous meteorology containing the study watershed can be constructed. The domain is used to identify and select storm events to use in the catalog and to define the limits of where events can be moved during stochastic simulations. Development of a transposition domain requires expert judgment and remains a subjective process until a repeatable, objective process is developed. The region must contain the study watershed in its entirety and be several times larger, with a recommended lower limit of 5 times the watershed area.
Three-Stage SOP Driven Domain Selection Approach
For SLAM-SIG, the approach begins by computing the geometric intersection of the 24 hr and 72 hr transposition domains, which defines the candidate TD at each GSL.
Notes: Mohsen

## Slide 4
Stage 1: Hard filter on the area ratio (AR > 5)
The SOP requires that the transposition domain have an area ratio greater than 5. This is an explicit pass/fail criterion. Apply it first and discard any GSL whose AR is at or below 5.
Stage 2: Meteorological review on the SOP-eligible candidates
For each candidate that survives Stage 1, the meteorologist visually evaluates whether the domain's climatology is consistent with the watershed's. The deliverables for this stage are visual aids that support expert judgment:
Plot the basin polygon together with the candidate polygon and the underlying PRISM precipitation / dewpoint / elevation envelope surface. Translate 3/3, 2/3. 1/3 into easily understandable labels.
The meteorologist selects one polygon. This step is judgment-based, and the documentation should record the meteorologist's reasoning rather than a numeric score.
Stage 3: Statistical QA on the selected polygon only
Once a single domain has been selected by Stages 1 and 2, distributional statistics (KS, Wasserstein, mean / median / quantile differences) can be reported as descriptive QA on that one polygon to characterize how its climatology compares with the basin.
These numbers go into the documentation and the final memo. The PRISM coverage fraction inside the selected polygon (and inside the basin) is noted, so any truncation effect is documented.
Notes: Mohsen

## Slide 5
Stage 1
Basin: Upper Tennessee (HUC 0601)
Notes: Mohsen

## Slide 6
Stage 2
Basin: Upper Tennessee (HUC 0601)
±5%
Notes: Mohsen

## Slide 7
Stage 3
Basin: Upper Tennessee (HUC 0601)
Summary of findings
Selected domain for Upper Tennessee: SLAM-SIG at GSL = 0.000, AR = 6.52, Tcap = 300 yr.
Stage 1 eliminated 18 of 20 candidate GSLs on the SOP requirement that AR > 5; only GSL = 0.000 and GSL = 0.025 remained.
Stage 2 envelope coverage shows the two survivors are climatologically near-identical inside their footprints. The larger polygon does not introduce a meaningfully different climatology.
Tcap distinguishes the survivors: GSL = 0.000 carries 50 yr more effective return-period reach than GSL = 0.025 at no climatological cost.
Stage 3 statistics describe the chosen polygon's climatology relative to the basin. The KS and Wasserstein values are reported as descriptive distance metrics.
Notes: Mohsen

## Slide 8
Selected Transposition Domain for Upper Tennessee (HUC 0601)
The valid transposition domain is the usable portion of the transposition domain. It includes only the locations where the watershed can be transposed while remaining fully within the selected transposition region.

## Slide 9
Stage 1
Basin: Allegheny (HUC 0501)
Clipped to CONUS Extent
Notes: Zach

## Slide 10
Stage 2
Basin: Allegheny (HUC 0501)
Clipped to CONUS Extent
±5%
Notes: Zach

## Slide 11
Selected GSL
Notes: Zach

## Slide 12
Geometrically Valid TD
Selected GSL TD

## Slide 13
Stage 3
Basin: Allegheny (HUC 0501)
Summary of findings
Selected domain for Allegheny: SLAM-SIG at GSL = 0.1, AR = 17.06, Tcap = 785 yr.
Stage 1 kept 18/20 candidate GSLs on the SOP requirement that AR > 5.
Stage 2 envelope coverage shows a plateau of climatologically similar survivors at GSLs >= 0.1. Smaller polygon beyond this point do not introduce a meaningfully different climatology.
Stage 3 statistics describe the chosen polygon's climatology relative to the basin using the geometrically valid domain derived from stormhub. The KS and Wasserstein values are reported as descriptive distance metrics.

## Slide 14
Clipped SLAM-SIG above 49th
GSL | TD area (mi^2) | Area Ratio (AR) | Status
0.000 | 737,367 | 30.52 | PASS (AR > 5)
0.025 | 415,970 | 17.22 | PASS (AR > 5)
0.050 | 370,225 | 15.32 | PASS (AR > 5)
0.075 | 100,264 | 4.15 | FAIL (AR <= 5)
0.100 | 96,563 | 4.00 | FAIL (AR <= 5)
0.125 | 87,245 | 3.61 | FAIL (AR <= 5)
0.150 | 84,247 | 3.49 | FAIL (AR <= 5)
0.175 | 82,030 | 3.39 | FAIL (AR <= 5)
0.200 | 78,288 | 3.24 | FAIL (AR <= 5)
0.225 | 78,006 | 3.23 | FAIL (AR <= 5)
0.250 | 76,702 | 3.17 | FAIL (AR <= 5)
0.275 | 75,884 | 3.14 | FAIL (AR <= 5)
0.300 | 70,558 | 2.92 | FAIL (AR <= 5)
0.325 | 70,357 | 2.91 | FAIL (AR <= 5)
0.350 | 68,388 | 2.83 | FAIL (AR <= 5)
0.375 | 65,359 | 2.70 | FAIL (AR <= 5)
0.400 | 63,902 | 2.64 | FAIL (AR <= 5)
0.425 | 50,057 | 2.07 | FAIL (AR <= 5)
0.450 | 49,412 | 2.04 | FAIL (AR <= 5)
0.475 | 46,705 | 1.93 | FAIL (AR <= 5)
Note: Clipping out Canada had no impact on which GSLs passed the AR > 5 test, just the AR values
Stage 1: South Platte (HUC 1019)
Notes: Erica

## Slide 15
Meteorological judgement: getting eastern-southeastern extent biggest concern. Dewpoint increases and elevation decreases as you move east -> different storm environments
GSL | AR | Pixels in TD | % Very similar (3/3) | % Mostly + Very (>=2/3) | Y (yr) | Tcap = Y * AR (yr)
0.050 | 15.32 | 1,546,422 | 91.9 | 99.2 | 46 | 705
0.025 | 17.22 | 1,728,117 | 88.0 | 96.6 | 46 | 792
0.000 | 30.52 | 2,928,855 | 68.8 | 92.2 | 46 | 1,404
Stage 2: South Platte (HUC 1019)
Notes: Erica

## Slide 16
Valid Transposition Domain: South Platte (HUC 1019)
Notes: Erica

## Slide 17
 | Precip Mean (in) | Precip Min (in) | Precip Max (in) | Elev Mean (ft) | Elev Min (ft) | Elev Max (ft) | Td Mean (F) | Td Min (F) | Td Max (F)
South Platte | 17.5 | 10.5 | 53.0 | 5926.3 | 2772.3 | 14009.2 | 28.9 | 6.8 | 36.8
SLAM-SIG GSL = 0.050 | 18.1 | 6.3 | 87.9 | 4502.4 | 1450.1 | 14019.0 | 29.2 | 4.8 | 39.5
 |  | KS Statistic | Wasserstein | Median Diff | 95th Pct Diff
Variable | Comparison |  |  |  | 
Precipitation (in) | South Platte vs. SLAM-SIG GSL = 0.050 | 0.1321 | 1.636 | -0.037 | -6.223
Elevation (ft) | South Platte vs. SLAM-SIG GSL = 0.050 | 0.4205 | 1435.373 | 1220.472 | 1466.535
Dewpoint (F) | South Platte vs. SLAM-SIG GSL = 0.050 | 0.1425 | 0.930 | 1.134 | -0.918
Stage 3: South Platte (HUC 1019)
Summary of findings:
Selected domain for South Platte: Valid area of SLAM-SIG at GSL = 0.05, AR = 14.84, Tcap = 683 years
Stage 1 kept 3/20 candidate GSLs on the SOP requirement that AR > 5 – no impact to number of passing GSLs from removing Canadian portions of domain
Stage 2 envelope coverage used to define eastern-southeastern extent
Stage 3 statistics describe the chosen polygon's climatology relative to the basin. The KS and Wasserstein values are reported as descriptive distance metrics
Notes: Erica

## Slide 18: EDH Discussion
Issue: Elements of the December 2025 FFRD SOP (Job Aid 2 – 1.4.2) indicate that FFRD should directly utilize and generally be in alignment with the priorities of USGS 3DHP. Aligning FFRD to USGS 3DHP could be very costly.
Discussion: An evaluation was performed by ARC in February 2025 to assess the alignment of FFRD and USGS 3DHP as well as provide recommendations for synergy between them.
Reference: December 2025 FFRD SOP – Job Aid 2 – Secion 1.4.2

## Slide 19: EDH Discussion
FFRD & USGS 3DHP Evaluation – February 2025
Goal: Evaluation of the potential benefits and challenges in shared hydrography efforts between FEMA’s Future of Flood Risk Data (FFRD) initiative and the U.S. Geological Survey (USGS) 3D National Hydrography Program (3DHP).
Findings:
  FFRD EDH was significantly cheaper than USGS 3DHP to produce.
  FFRD EDH is too coarse to benefit USGS 3DHP.
  Existing USGS 3DHP could be leveraged for FFRD EDH but would need to be filtered or modified.
    Streamlines: 3DHP can be leveraged for FFRD but vertices would need to be filtered.
    Hydroconnectors: Both efforts provide minimal benefit to each other. 3DHP hydroconnectors could be leveraged but width is not important to 3DHP so those would have to be adjusted for FFRD. Also, placement would need to be reviewed since 3DHP terrain is in a metric resolution where as FFRD is in feet.
    Breaklines: Neither efforts provide much value to each other. Breaklines are not an influential layer to 3DHP.

## Slide 20: EDH Discussion
Suggested Updates and Clarification:
Update text within the FFRD SOP to suggest leveraging existing USGS 3DHP data with some filtering and modification for use in FFRD.
Where USGS 3DHP is not available, EDH would generally be autogenerated using the following general process:
      Use FFRD SOP Terrain (4ft Resolution)
      Apply Hydro-Enforcement
        Incorporate Bathymetry Where Available
        Hydro-connections
      Use ArcHydro (or other industry standard processes) to delineate the EDH.
      Post-Processing (General Cleaning & Smoothing)

## Slide 21: References
ARC, Compass, and STARR II (Joint PTS). (2025, December). Validation Basin(s) – Hydrology First Prospectus (Final, December 12, 2025).
ARC, COMPASS, & STARR II (Joint PTS). (2026, February). FFRD SOP: Proposed terrain tiling standards. FEMA Future of Flood Risk Data Program. Internal memorandum.
Federal Emergency Management Agency & U.S. Army Corps of Engineers. (2025, December). Future of Flood Risk Data methodology standard operating procedure—Inland (Volume II: Technical standards and procedures, Version 1 draft).
STARR II. (2026, March). South Platte Transposition Domain Investigation. FEMA Future of Flood Risk Data Program. Internal memorandum.
Williams, T. (n.d.). ffrd-grid-tiling [Source code]. GitHub. https://github.com/fema-ffrd/ffrd-grid-tiling
Wright, D. B., FitzGerald, B., & Yan, L. (2025). Advancing the science of extreme storms for hydrological and hydraulic modeling: Year 1 (1 September 2025—30 November 2025) Deliverables D1, D2, and D3 (DHS Coastal Resilience Center Report). University of Wisconsin–Madison. FEMA Contract No. 70RSAT21G00000013.

## Slide 22: Meeting References
Federal Emergency Management Agency, U.S. Army Corps of Engineers, & Joint PTS Team (ARC, COMPASS, and STARR II). (2026a, February 20).FFRD Validation Basin bi‑weekly meeting transcript and recording. Internal project record.
Federal Emergency Management Agency, U.S. Army Corps of Engineers, & Joint PTS Team (ARC, COMPASS, and STARR II). (2026b, March 6).FFRD Validation Basin bi‑weekly meeting transcript and recording. Internal project record.
Federal Emergency Management Agency, U.S. Army Corps of Engineers, & Joint PTS Team (ARC, COMPASS, and STARR II). (2026c, April 17).FFRD Validation Basin bi‑weekly meeting transcript and recording. Internal project record.
Federal Emergency Management Agency, U.S. Army Corps of Engineers, & Joint PTS Team (ARC, COMPASS, and STARR II). (2026d, May 1).FFRD Validation Basin bi‑weekly meeting transcript and recording. Internal project record.